## Slide 1
CN Controller
CN Panel Jack
USB Panel Jack
GPS Antenna
USB Panel Jack
External
Speaker
ASW-27 N227BB
Avionics Functional Block Diagram
1/29/19 JHDeRosa
OAT
Power
Cambridge 302
ClearNav Display
ClearNav Vario ADC
ClearNav Vario
GPS Antenna
External
Speaker
FLARM Core
Power
CAN
GPS Antenna
Power
FLARM A
Antenna
ADS-B
Antenna
RJ45 Panel Jack
Power
GPS Antenna

## Slide 2
ASW-27 N227BB
Avionics Shelf
1/29/19 JHDeRosa

## Slide 3
ASW-27 N227BB
Avionics Power Distribution
Battery A Bus
(Navigation)
Battery Ground
Bus
Battery B Bus
(Communications)
To Avionics
+
12Vdc
Battery A
(Navigation)
+
Battery Bus
Bridging
Switch*
Battery B
Bat A Connected
Bat B Connected
Master Breaker/Switch 5A
(TYCO Model W31)
Master Breaker/Switch 5A
(TYCO Model W31)
12Vdc
Battery B
(Communications)
Schottky 1N5821 Diode
Schottky 1N5821 Diode
1/29/19 JHDeRosa
** GliderGuider LED Battery Monitor (http://www.gliderguider.net)
GliderGuider
LED Battery
Monitor**
GliderGuider
LED Battery
Monitor**
* The Battery Bus Bridging Switch is used to tie the two power buses together and,
by using the two diodes, not allowing cross charging of the batteries

## Slide 4
ASW-27 N227BB
Avionics Power Distribution
Positive Battery A
Connections
Negative Battery
& Ground Connections
Positive Battery B
Connections
Breaker Switch
Navigation Bus
Breaker Switch
Communications Bus
Battery Bus
Bridging
Switch
1/29/19 JHDeRosa